## Slide 1: Overview
1
Register Transfer Language
Register Transfer
Bus and Memory Transfers
Arithmetic Micro-operations
Logic Micro-operations
Shift Micro-operations
Arithmetic Logic Shift Unit

## Slide 2: Logic Micro operations
2

## Slide 3: Logic Microoperations
3

## Slide 4: Hardware Implementation
4
S1 | S0 | Output | -operation
0 | 0 | F = A  B | AND
0 | 1 | F = A  B | OR
1 | 0 | F = A Ⓒ B | XOR
1 | 1 | F = A’ | Complement
Function table
S 1
S 0
Ai B i
0
1
4 X 1 F i MUX
2
3 Select

## Slide 5: Applications of Logic Microoperations
5
Logic microoperations can be used to manipulate individual bits or a portions of a word in a register
Consider the data in a register A. In another register, B, is bit data that will be used to modify the contents of A
Selective-set
Selective-complement
Selective-clear
Mask (Delete)
Clear
Insert
Compare
A  A + B
A  A Ⓒ B A  A • B’ A  A • B A  A Ⓒ B
A  (A • B) + C
A  A Ⓒ B

## Slide 6
Applications of Logic Microoperations
1. In a selective set operation, the bit pattern in B is used to set certain bits in A 1 1 0 0 At 1 0 1 0 B 1 1 1 0 At+1 (A  A + B) If a bit in B is set to 1, that same position in A gets set to 1, otherwise that
2. Inbiat isnelAeckteiveepscoitms plreemvieonuts ovpaleureation, the bit pattern in B is used to complement certain bits in A 1 1 0 0 At 1 0 1 0 B 0 1 1 0 At+1 (A  A Ⓒ B) If a bit in B is set to 1, that same position in A gets complemented from its original value, otherwise it is unchanged
6

## Slide 7
Applications of Logic Microoperations
3. In a selective clear operation, the bit pattern in B is used to clear certain bits in A 1 1 0 0 At 1 0 1 0 B 0 1 0 0 At+1 (A  A  B’) If a bit in B is set to 1, that same position in A gets set to 0, otherwise it is unchanged
4. In a mask operation, the bit pattern in B is used to clear certain bits in A 1 1 0 0 At 1 0 1 0 B 1 0 0 0 At+1 (A  A  B) If a bit in B is set to 0, that same position in A gets set to 0, otherwise it is unchanged
7

## Slide 8: Applications of Logic Microoperations
8
5. In a clear operation, if the bits in the same position in A and B are the same, they are cleared in A, otherwise they are set in A
1 1 0 0 At
1 0 1 0 B
0 1 1 0
At+1
(A  A Ⓒ B)

## Slide 9: Applications of Logic Microoperations
9
6. An insert operation is used to introduce a specific bit pattern into A register, leaving the other bit positions unchanged
This is done as
–
–
–
A mask operation to clear the desired bit positions, followed by
An OR operation to introduce the new bits into the desired positions Example
•
•
Suppose you wanted to introduce 1010 into the low order four bits of A: 1101 1000 1011 0001 A (Original)
1101 1000 1011 1010 |  |  | A (Desired) |  | 
• | 1101 1000 | 1011 | 0001 |  | A (Original)
 | 1111 | 1111 | 1111 | 0000 | Mask
 | 1101 | 1000 | 1011 | 0000 | A (Intermediate)
 | 0000 | 0000 | 0000 | 1010 | Added bits
 | 1101 | 1000 | 1011 | 1010 | A (Desired)

## Slide 10: Shift Microoperations
10
•
There are three types of shifts
–
–
–
Logical shift Circular shift Arithmetic shift
•
What differentiates them is the information that goes into the serial input
Serial
input
A right shift operation
A left shift operation
Serial input

## Slide 11: Logical Shift
11
•
In a logical shift the serial input to the shift is a 0.
•
A right logical shift operation:
•
A left logical shift operation:
•
In a Register Transfer Language, the following notation is used
for a logical shift left for a logical shift right
–
–
–
shl shr
Examples:
•
•
R2  shr R2 R3  shl R3
0
0

## Slide 12: Circular Shift
12
•
In a circular shift the serial input is the bit that is shifted out of the other end of the register.
•
A right circular shift operation:
•
A left circular shift operation:
•
In a RTL, the following notation is used
for a circular shift left for a circular shift right
–
–
–
cil cir
Examples:
•
•
R2  cir R2 R3  cil R3

## Slide 13: Arithmetic Shift
13
•
•
•
•
•
An arithmetic shift is meant for signed binary numbers (integer) An arithmetic left shift multiplies a signed number by two
An arithmetic right shift divides a signed number by two Sign bit : 0 for positive and 1 for negative
The main distinction of an arithmetic shift is that it must keep the sign of the number the same as it performs the multiplication or division
•
A right arithmetic shift operation:
•
A left arithmetic shift operation:
0
sign bit
sign bit

## Slide 14: Arithmetic Shift
14
•
An left arithmetic shift operation must be checked for the overflow
0
V
Before the shift, if the leftmost two bits differ, the shift will result in an overflow
In a RTL, the following notation is used
for an arithmetic shift left for an arithmetic shift right
ashl
ashr
– Examples:
» R2  ashr R2
» R3  ashl R3
sign bit

## Slide 15: Hardware Implementation of Shift Microoperation
15

## Slide 16: Arithmetic Logic and Shift Unit
16
Arithmetic Circuit
Logic Circuit
Select
0
1
2
3
4 x 1 F
MUX
S3 S2
S1
S0
A
C i
E
shr
shl
C i+1
i
B i
i
A i+1
D i
A i-1
i
s2 | s3 | Operation
0 | 0 | Arithmetic
0 | 1 | Logical
1 | 0 | Shr
1 | 1 | shl