## Slide 2: Overview
Control Unit
2
General Register Organization
Stack Organization
Instruction Formats
Addressing Modes
Data Transfer and Manipulation
Program Control
RISC and CISC

## Slide 3: Major Components of CPU
Central Processing Unit
3
Storage Components
Registers
Flags
Execution (Processing) Components
Arithmetic Logic Unit(ALU)
Arithmetic calculations, Logical computations, Shifts/Rotates
Transfer Components
Bus
Control Components
Control Unit

## Slide 4: Register
Central Processing Unit
4
In Basic Computer, there is only one general purpose register, the Accumulator (AC)
In modern CPUs, there are many general purpose registers
It is advantageous to have many registers
  Transfer between registers within the processor are relatively fast
  Going “off the processor” to access memory is much slower

## Slide 5: Processor Organization
Central Processing Unit
5
In general, most processors are organized in one of 3 ways
  Single register (Accumulator) organization
    Basic Computer is a good example
    Accumulator is the only general purpose register
  General register organization
    Used by most modern computer processors
    Any of the registers can be used as the source or destination for computer operations
  Stack organization
    All operations are done using the hardware stack
    For example, an OR instruction will pop the two top elements from the
stack, do a logical OR on them, and push the result on the stack

## Slide 6: General Register Organization
Central Processing Unit 6
MUX
SELA
{
MUX
} SELB
ALU
OPR
R1 R2
R3
R4
R5
R6
R7
Input
3 x 8 decoder
SELD
Load (7 lines)
Output
A bus B bus
Clock

## Slide 7: Operation of ControlUnit
Central Processing Unit
8
The control unit
Directs the information flow through ALU by
Selecting various Components in the system
Selecting the Function of ALU
Example: R1  R2 + R3
MUX A selector (SELA): BUS A  R2
MUX B selector (SELB): BUS B  R3
ALU operation selector (OPR): ALU to ADD
Decoder destination selector (SELD): R1  Out Bus
Control Word
Encoding of register selection fields
SELA | SELB | SELD | OPR
3 3 3 5
Binary Code | SELA | SELB | SELD
000 | Input | Input | None
001 | R1 | R1 | R1
010 | R2 | R2 | R2
011 | R3 | R3 | R3
100 | R4 | R4 | R4
101 | R5 | R5 | R5
110 | R6 | R6 | R6
111 | R7 | R7 | R7

## Slide 8
Central Processing Unit
9
ALU Control Encoding of ALU operations OPR Select Operation 00000 Transfer A 00001 Increment A 00010 ADD A + B 00101 Subtract A - B 00110 Decrement A 01000 AND A and B 01010 OR A and B 01100 XOR A and B 01110 Complement A 10000 Shift right A 11000 Shift left A Examples of ALU Microoperations |  |  | Symbol |  |  |  | 
 |  |  | TSFA |  |  |  | 
 |  |  | INCA |  |  |  | 
 |  |  | ADD |  |  |  | 
 |  |  | SUB |  |  |  | 
 |  |  | DECA |  |  |  | 
 |  |  | AND |  |  |  | 
 |  |  | OR |  |  |  | 
 |  |  | XOR |  |  |  | 
 |  |  | COMA |  |  |  | 
 |  |  | SHRA |  |  |  | 
 |  |  | SHLA |  |  |  | 
 | Microoperation | Symbolic Designation SELA SELB SELD OPR | Control Word |  |  |  | 
 | R1  R2  R3 | R2 R3 R1 SUB | 010 | 011 | 001 | 00101 | 
 | R4  R4  R5 | R4 R5 R4 OR | 100 | 101 | 100 | 01010 | 
 | R6  R6 + 1 | R6 - R6 INCA | 110 | 000 | 110 | 00001 | 
 | R7  R1 | R1 - R7 TSFA | 001 | 000 | 111 | 00000 | 
 | Output  R2 | R2 - None TSFA | 010 | 000 | 000 | 00000 | 
 | Output  Input | Input - None TSFA | 000 | 000 | 000 | 00000 | 
 | R4  shl R4 | R4 - R4 SHLA | 100 | 000 | 100 | 11000 | 
 | R5  0 | R5 R5 R5 XOR | 101 | 101 | 101 | 01100 | 

## Slide 9: Stack Organization
Central Processing Unit
10
Stack
Very useful feature for nested subroutines, nested interrupt services
Also efficient for arithmetic expression evaluation
Storage which can be accessed in LIFO
Pointer: SP
Only PUSH and POP operations are applicable
Stack Organization
  Register Stack Organization
  Memory Stack Organization

## Slide 10: Register Stack Organization
Central Processing Unit
12
Push, Pop operations
/* Initially, SP = 0, EMPTY = 1, FULL = 0 */
PUSH
SP M[SP]
SP + 1
DR
POP
DR M[SP]
SP SP  1
If (SP = 0) then (FULL 1) EMPTY 0
If (SP = 0) then (EMPTY 1) FULL 0
C
B
A
4
3
2
1
0
63
FULL
EMPTY
SP
DR
Flags
Stack pointer
6 bits

## Slide 11: Memory Stack Organization
Central Processing Unit
13
- A portion of memory is used as a stack with a
processor register as a stack pointer
- PUSH:
- POP:
SP  SP - 1 M[SP]  DR
DR  M[SP]
SP  SP + 1
Memory with Program, Data, and Stack Segments
3000
Program (instructions)
Data (operands)
1000
PC
AR
SP
stack
3997
3998
3999
4000
4001
- Most computers do not provide hardware to check stack overflow (full stack) or underflow (empty stack)  must be done in software

## Slide 12: Reverse Polish Notation
Central Processing Unit
14
Stack is very effective in evaluating arithmetic expressions
Arithmetic Expressions:
A * B + C * D
Polish Notation ( Prefix ) : Place operator before operand Reverse Polish Notation (Postfix) : Place operator after operand
AB*CD*+
1. (A*B)CD*+
2. (A*B) (C*D) +
3. (A*B) + (C*D)
(A+B) * [C* (D+E)+ F] 
AB+DE+C*F+*

## Slide 13: Reverse Polish Notation
Central Processing Unit
15
A + B
+ A B A B +
Infix notation
Prefix or Polish notation
Postfix or reverse Polish notation
- The reverse Polish notation is very suitable for stack manipulation
Evaluation of Arithmetic Expressions
Any arithmetic expression can be expressed in parenthesis-free Polish notation, including reverse Polish notation
(3 * 4) + (5 * 6)  3 4 * 5 6 * +
Arithmetic Expressions: A + B
3
12
42
4
3
5
12
6
5
12
30
12
3
4
*
5
6
*
+

## Slide 14: Instruction Format
Central Processing Unit
17
Mode field
- determines how the address field is to be interpreted (to get effective address or the operand)
The number of address fields in the instruction format depends on the internal
organization of CPU
The three most common CPU organizations:
Single accumulator organization:
ADD X /* AC  AC + M[X] */
General register organization:
ADD | R1, R2, R3 | /* R1  R2 + R3 */
ADD | R1, R2 | /* R1  R1 + R2 */
MOV | R1, R2 | /* R1  R2 */
ADD | R1, X | /* R1  R1 + M[X] */
/* TOS  M[X] */
Stack organization: PUSH X
ADD
Instruction Fields
OP-code field - specifies the operation to be performed
Address field - designates memory address(es) or a processor register(s)

## Slide 15: Three & Two Address Instruction
Central Processing Unit 18
Three-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
ADD | R1, A, B | /* R1  M[A] + M[B] */ | 
ADD | R2, C, D | /* R2  M[C] + M[D] */ | 
MUL | X, R1, R2 | /* M[X]  R1 * R2 | */
Results in short programs
Instruction becomes long (many bits)
Two-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
MOV | R1, A | /* R1  M[A] | */
ADD | R1, B | /* R1  R1 + M[A] | */
MOV | R2, C | /* R2  M[C] | */
ADD | R2, D | /* R2  R2 + M[D] | */
MUL | R1, R2 | /* R1  R1 * R2 | */
MOV | X, R1 | /* M[X]  R1 | */
-most common in commercial computer

## Slide 16: One Address Instruction
Central Processing Unit
19
One-Address Instructions
  Use an implied AC register for all data manipulation
  Program to evaluate X = (A + B) * (C + D) :
LOAD | A | /* | AC  M[A] */ |  | 
ADD | B | /* | AC  AC + M[B] | */ | 
STORE | T | /* | M[T]  AC */ |  | 
LOAD | C | /* | AC  M[C] */ |  | 
ADD | D | /* | AC  AC + M[D] |  | */
MUL | T | /* | AC  AC * M[T] |  | */
STORE | X | /* | M[X]  AC */ |  | 

## Slide 17: Zero Address Instruction
Central Processing Unit
21
Zero-Address Instructions
  Can be found in a stack-organized computer
  Program to evaluate X = (A + B) * (C + D) :
PUSH | A | /* | TOS  A | */
PUSH | B | /* | TOS  B | */
ADD PUSH | C | /* /* | TOS  (A + TOS  C | B)*/ */
PUSH | D | /* | TOS  D | */
ADD |  | /* | TOS  (C + | D)*/
MUL POP
X
/* TOS  (C + D) * (A + B) */
/* M[X]  TOS */

## Slide 18: Addressing Mode
Central Processing Unit
22
Addressing Modes
- Specifies a rule for interpreting or modifying the address field of the instruction (before the operand is actually referenced)
Computer uses Addressing mode to accommodate one or both of the following provision :
To give flexibility to programmer by providing facilities such as pointer to memory, counter for loop control, indexing of data, program relocation
To reduce no. of bits in addressing fields of the instruction

## Slide 19: Addressing Mode
Central Processing Unit
23
Two modes that need no address field at all :
Implied Mode
  Address of the operands are specified implicitly in the definition of the instruction
  No need to specify address in the instruction
  EA = AC, or EA = Stack[SP]
  Examples from Basic Computer - CLA, CME
Immediate Mode
  Instead of specifying the address of the operand,
operand is specified in the instruction itself.
  No need to specify address in the instruction
  However, operand itself needs to be specified
  Sometimes, require more bits than the address
  Fast to acquire an operand

## Slide 20: Addressing Mode
Central Processing Unit
24
Register Mode
  When address field specifies a processor register, it is said to be in register mode
  Designated operand need to be in a register
  Shorter address than the memory address
  Saving address field in the instruction
  Faster to acquire an operand than the memory addressing
  EA = IR(R) (IR(R): Register field of IR)
Register Indirect Mode
  Instruction specifies a register which contains the memory address of the operand
  Saving instruction bits since register address is shorter than the memory address
  Slower to acquire an operand than both the register addressing or memory addressing
    Adv : Fewer address bit reqd. compared to memory address
    EA = [IR(R)] ([x]: Content of x)
Autoincrement or Autodecrement Mode
  Similar to Register Indirect but When the address in the register is used to access memory, the value in the register is incremented or decremented by 1 automatically

## Slide 21: Addressing Mode
Central Processing Unit
25
Direct Address Mode
  Instruction specifies the memory address which can be used directly to access the operand
  Faster than the other memory addressing modes
  Too many bits are needed to specify the address for a large physical memory space
  EA = IR(addr) (IR(addr): address field of IR)
Indirect Addressing Mode
  The address field of an instruction specifies the address of a memory location that
contains the address of the operand
  When the abbreviated address is used large physical memory can be addressed with a relatively small number of bits
  Slow to acquire an operand because of an additional memory access
  EA = M[IR(address)]

## Slide 22: Addressing Mode
Central Processing Unit
26
Relative Addressing Modes
  The Address fields of an instruction specifies the part of the address (abbreviated address) which can be used along with a designated register to calculate the address of the operand
  Address field of the instruction is short
  Large physical memory can be accessed with a small number of address bits
  EA = f(IR(address), R), R is sometimes implied
-3 different Relative Addressing Modes depending on R;
PC Relative Addressing Mode (R = PC)
    EA = PC + IR(address) Adv : Shorter Address Field
Indexed Addressing Mode (R = IX, where IX: Index Register)
    EA = IX + IR(address)
Base Register Addressing Mode
(R = BAR, where BAR: Base Address Register)
    EA = BAR + IR(address)

## Slide 23: Central Processing Unit
27
Addressing Effective Mode Address |  | Content of AC
Direct address 500 | /* AC  (500) */ | 800
Immediate operand - |  | 
Indirect address |  | 
Relative address |  | 
Indexed address |  | 
Register -- |  | 
Register indirect |  | 
Autodecrement |  | 
Autoincrement |  | 
200
201
202
399
400
500
600
702
800
Load to AC | Mode
Address = 500 | 
Next instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
Memory
Addressing Mode - Example
Address
PC = 200
R1 = 400
RX = 100
AC

## Slide 24: Central Processing Unit
28
Addressing Effective Mode Address |  |  |  |  | Content of AC
Direct address Immediate operand Indirect address Relative address Indexed address Register Register indirect Autodecrement Autoincrement | 500 - 800 702 600 - 400 399 400 | /* AC /* AC /* AC /* AC /* AC /* AC /* AC /* AC /* AC |  (500)  500  ((500))  (PC+500)  (RX+500)  R1  (R1)  -(R)  (R1)+ | */ */ */ */ */ */ */ */ */ | 800 500 300 325 900 400 700 450 700
200
201
202
399
400
500
600
702
800
Load to AC | Mode
Address = 500 | 
Next instruction | 
450 | 
700 | 
800 | 
900 | 
325 | 
300 | 
Memory
Addressing Mode - Example
Address
PC = 200
R1 = 400
RX = 100
AC

## Slide 25: Overview
Control Processing Unit
29
General Register Organization
Stack Organization
Instruction Formats
Addressing Modes
Data Transfer and Manipulation
Program Control
RISC and CISC

## Slide 26: Data Transfer and Manipulation
Central Processing Unit 30
Instruction set of different computers differ from each other mostly in way the operands are determined from the address and mode fields.
The basic set of operations available in a typical computer are :
Data Transfer Instructions
Data Manipulation Instruction :
perform arithmetic, logic and shift operation
Program Control Instructions
decision making capabilities, change the path taken by the program when executed in computer.

## Slide 27: Data Transfer Instructions
Central Processing Unit
31
Name | Mnemonic
Load | LD
Store | ST
Move | MOV
Exchange | XCH
Input | IN
Output | OUT
Push | PUSH
Pop | POP
Move data from one place in computer to another without changing
the data content
Most common transfer : processor reg -memory, processor reg -I/O,
between processor register themselves
Typical Data Transfer Instructions

## Slide 28: Data Transfer Instructions
Central Processing Unit
32
Mode | Assembly Convention | Register Transfer
Direct address | LD ADR | AC  M[ADR]
Indirect address | LD @ADR | AC  M[M[ADR]]
Relative address | LD $ADR | AC  M[PC + ADR]
Immediate operand | LD #NBR | AC  NBR
Index addressing | LD ADR(X) | AC  M[ADR + XR]
Register | LD R1 | AC  R1
Register indirect | LD (R1) | AC  M[R1]
Autoincrement | LD (R1)+ | AC  M[R1], R1  R1 + 1
Autodecrement | LD -(R1) | R1  R1 - 1, AC  M[R1]
Data Transfer Instructions with Different Addressing Modes
Some assembly language conventions modify the mnemonic symbol to differentiate
between the different addressing modes

## Slide 29: Data Maniplulation Instructions
Central Processing Unit 33
Three Basic Types:
  Arithmetic instructions
  Logical and bit manipulation instructions
  Shift instructions
These instruction performs operation on data and provide the computational
capabilities for the computer

## Slide 30: Data Manipulation Instructions
Central Processing Unit 34
Arithmetic Instructions
Name | Mnemonic
Increment | INC
Decrement | DEC
Add | ADD
Subtract | SUB
Multiply | MUL
Divide | DIV
Add with Carry | ADDC
Subtract with Borrow | SUBB
Negate(2’s Complement) | NEG
Four basic arithmetic operations :
+ - * /

## Slide 31: Data Manipulation Instructions
Central Processing Unit 35
Name | Mnemonic
Clear | CLR
Complement | COM
AND | AND
OR | OR
Exclusive-OR | XOR
Clear carry | CLRC
Set carry | SETC
Complement carry | COMC
Enable interrupt | EI
Disable interrupt | DI
Logical Instructions perform binary operations on string of bits stored in registers
Useful for manipulating individual/ group of bits
 Consider each bit separately
Logical and Bit Manipulation Instructions
AND Clear selected bits OR Set selected bits
XOR Complement selected bits

## Slide 32: Data Manipulation Instructions
Central Processing Unit 36
Name | Mnemonic
Logical shift right | SHR
Logical shift left | SHL
Arithmetic shift right | SHRA
Arithmetic shift left | SHLA
Rotate right | ROR
Rotate left | ROL
Rotate right thru carry | RORC
Rotate left thru carry | ROLC
Shift Instructions

## Slide 33: Program Control Instruction
Central Processing Unit
37
PC
+1
In-Line Sequencing (Next instruction is fetched from the
next adjacent location in the memory)
Address from other source; Current Instruction, Stack, etc; Branch, Conditional Branch, Subroutine, etc
Program Control Instructions
Name | Mnemonic
Branch | BR
Jump | JMP
Skip | SKP
Call | CALL
Return | RTN
Compare(by  ) | CMP
Test(by AND) | TST
* CMP and TST instructions do not retain their results of operations (  and AND, resp.).
They only set or clear certain Flags.
like carry /sign/zero bit or overflow condition

## Slide 34: Flag, Processor Status Word
Central Processing Unit 38
In Basic Computer, the processor had several (status) flags – 1 bit value that indicated various information about the processor’s state – FGI, FGO, I, IEN, R
In some processors, flags like these are often combined into a register – the processor status register (PSR); sometimes called a processor status word (PSW)
Common flags in PSW are
C (Carry): Set to 1 if the carry out of the ALU is 1
S (Sign): The MSB bit of the ALU’s output
Z (Zero): Set to 1 if the ALU’s output is all 0’s
V (Overflow): Set to 1 if there is an overflow
Status Flag Circuit
c7
c8
A
8
B
8
V | Z | S | C
F7
8-bit ALU F7 - F0
8
F
Check for zero output

## Slide 35: Status Bit Condition
Central Processing Unit
39
Status Bit | Description | Set to 1 | Clear to 0
C | Carry | If end carry C8 =1 | If carry=0
S | Sign | Highest order bit F7=1 | If F7=0
Z | Zero | O/P of ALU contains all 0 | otherwise
V | Overflow | EX-OR of last two carries=1 | otherwise

## Slide 36: Conditional Branch Instruction
Central Processing Unit 40
Mnemonic Branch condition Tested condition
BZ Branch if zero Z = 1 BNZ Branch if not zero Z = 0 BC Branch if carry C = 1 BNC Branch if no carry C = 0 BP Branch if plus S = 0 BM Branch if minus S = 1 BV Branch if overflow V = 1 BNV Branch if no overflow V = 0
Unsigned compare conditions (A - B) BHI Branch if higher A > B BHE Branch if higher or equal A  B BLO Branch if lower A < B BLOE Branch if lower or equal A  B BE Branch if equal A = B BNE Branch if not equal A  B
Signed compare conditions (A - B) BGT Branch if greater than A > B BGE Branch if greater or equal A  B BLT Branch if less than A < B BLE Branch if less or equal A  B BE Branch if equal A = B BNE Branch if not equal A  B

## Slide 37: Central Processing Unit
41
Subroutine Call and Return
Call subroutine
Jump to subroutine
Branch to subroutine
Branch and save return address
Subroutine Call
Instructions are executed by performing two operations :
  Save PC as Return Address to get the address of the location in the Calling Program upon exit from the Subroutine
  Branch to the beginning of the Subroutine
- Same as the Branch or Conditional Branch
Locations for storing Return Address
  First Location in the subroutine (Memory)
  Fixed Location in memory
  In a processor Register
  In memory stack
- most efficient way
CALL
SP  SP - 1 M[SP]  PC PC  EA
RTN
PC  M[SP] SP  SP + 1
Subroutine : self contained sequence of instructions that performs a given computation task

## Slide 38
Central Processing Unit
42
Interrupt Procedure
Program Interrupt refers to the transfer of program control from a currently running program to another service program as a result of an external or internal generated request

## Slide 39: Interrupt Procedure
Central Processing Unit
43
Interrupt Procedure and Subroutine Call
The interrupt is usually initiated by an internal or an external signal rather than from
the execution of an instruction (except for the software interrupt)
The address of the interrupt service program is determined by the hardware rather than from the address field of an instruction
An interrupt procedure usually stores all the information necessary to define the state of CPU rather than storing only the PC.
The state of the CPU is determined from:
  Content of the PC
  Content of all processor registers
  Content of status bits
Many ways of saving the CPU state depending on the CPU architectures

## Slide 40: Interrupt Procedure
Central Processing Unit
44
CPU does not respond to interrupt until end of instruction cycle, checks just before next fetch phase
If interrupt pending, control passed to h/w interrupt cycle:
  Content of PC and PSW is pushed into stack
  branch address of interrupt transferred to PC and new PSW loaded into status registers
Service Program executed starting from branch address and status of CPU as specified by new PSW
Last instruction from service program is return from interrupt
instruction

## Slide 41: Central Processing Unit
45
Program Interrupt
Types of Interrupts External interrupts
External Interrupts initiated from the outside of CPU and Memory
I/O Device → Data transfer request or Data transfer complete
Timing Device → Timeout
Power supply  Power Failure
Internal interrupts (traps)
Internal Interrupts are arises from illegal or erroneous use of instn. or data
- initiated by program itself rather than external event
Register, Stack Overflow
Divide by zero
OP-code Violation
Protection Violation
Software Interrupts
Both External and Internal Interrupts are initiated by the computer HW. Software Interrupts are initiated by the executing an instruction.
- Supervisor Call
Switching from a user mode to the supervisor mode
Allows to execute a certain class of operations
which are not allowed in the user mode

## Slide 42: RISC- Historical BackGround
Central Processing Unit
46
High-Level Language
Hardware
Instruction
Set
Architecture
IBM System/360, 1964
The real beginning of modern computer architecture
Distinction between Architecture and Implementation
Architecture: The abstract structure of a computer
seen by an assembly-language programmer
Hardware
-program
Compiler
Hardware
Implementation
Continuing growth in semiconductor memory and microprogramming
 A much richer and complicated instruction sets
 CISC(Complex Instruction Set Computer)

## Slide 43: CISC
Central Processing Unit
47
Arguments Advanced at that time
Richer instruction sets would simplify compilers
Richer instruction sets would alleviate the software crisis
– move as much functions to the hardware as possible
Richer instruction sets would improve architecture quality
CISC
These computers with many instructions and addressing modes came to be known as Complex Instruction Set Computers (CISC)
One essential goal for CISC machines was to provide a single machine
instruction for each statement that is written in high level language.
Another characteristic was incorporation of variable length instruction format.

## Slide 44: Complex Instruction Set Computers
Central Processing Unit 48
Another characteristic of CISC computers is that they have instructions that
act directly on memory addresses
  For example,
ADD L1, L2, L3
that takes the contents of M[L1] adds it to the contents of M[L2] and stores the result in location M[L3]
An instruction like this takes three memory access cycles to execute
That makes for a potentially very long instruction execution cycle
The problems with CISC computers are
  The complexity of the design may slow down the processor,
  The complexity of the design may result in costly errors in the processor design and
implementation,
  Many of the instructions and addressing modes are used rarely, if ever

## Slide 45: Summary : Criticism On CISC
Central Processing Unit
49
High Performance General Purpose Instructions
Complex Instruction
→ Format, Length, Addressing Modes
→ Complicated instruction cycle control due to the complex decoding HW and decoding process
Multiple memory cycle instructions
→ Operations on memory data
→ Multiple memory accesses/instruction
Microprogrammed control is necessity
→ Microprogram control storage takes substantial portion of CPU chip area
→ Semantic Gap is large between machine instruction and microinstruction
- General purpose instruction set includes all the features required by individually different applications
→ When any one application is running, all the features required by the other
applications are extra burden to the application

## Slide 46: RISC – Reduced Instruction Set Computers
Central Processing Unit 50
In the late ‘70s and early ‘80s there was a reaction to the shortcomings
of the CISC style of processors
Reduced Instruction Set Computers (RISC) were proposed as an
alternative
The underlying idea behind RISC processors is to simplify the instruction set and reduce instruction execution time
RISC processors often feature:
  Few instructions
  Few addressing modes
  Only load and store instructions access memory
  All other operations are done using on-processor registers
  Fixed length instructions
  Single cycle execution of instructions
  The control unit is hardwired, not microprogrammed

## Slide 47: RISC – Reduced Instruction Set Computers
Central Processing Unit 51
Since all but the load and store instructions use only registers for operands, only a few addressing modes are needed
By having all instructions the same length, reading them in is easy and fast
The fetch and decode stages are simple
The instruction and address formats are designed to be easy to decode
Unlike the variable length CISC instructions, the opcode and register fields of RISC instructions can be decoded simultaneously
The control logic of a RISC processor is designed to be simple and fast
The control logic is simple because of the small number of instructions and the simple addressing modes
The control logic is hardwired, rather than microprogrammed, because
hardwired control is faster