## Slide 1: Input-Output Organization -UNIT 4
1
Input-Output Interface
Asynchronous Data Transfer
Modes of Transfer
Priority Interrupt
Direct Memory Access
Input-Output Processor

## Slide 2: Modes of Transfer
Data transfer between central computer and I/O devices may be handled in a variety of modes.
Some modes use CPU as intermediate path
and others transfer data directly to and from memory unit.
Data Transfer to or from peripheral can be handled in one of three possible modes :
Programmed I/O
Interrupt-Initiated I/O
Direct Memory Access (DMA)

## Slide 7: Programmed I/O method
In programmed I/O method, CPU stays in a program loop until the I/O unit indicated that it is ready for data transfer.
This is a time consuming process since it keeps the processor busy needlessly.
It can be avoided by using Interrupt facility and special commands to inform the interface to issue
an interrupt request signal when data are available for the device.

## Slide 8
Q-In programmed I/O , CPU reads the data from data register , if flag is equal to
A= 0 B=1

## Slide 9
An alternative to the CPU constantly monitoring the flag is to let the interface inform the computer when it is ready to transfer data.
This mode of transfer uses the interrupt facility. While the CPU is running a program, it does not check the flag.
However, when the flag is set, the computer is momentarily interrupted from proceeding with the current program and is informed of the fact that the flag has been set.
The CPU deviates from what it is doing to take care of the input or output transfer.
After the transfer is completed, the computer returns to the previous program to continue what it was doing before the interrupt.
The CPU responds to the interrupt signal by storing the return address from the program counter into a memory stack and then control branches to a service routine that processes the required I/O transfer.

## Slide 10
In principle, there are two methods for accomplishing the way that the processor chooses the branch address of the service routine varies from one unit to another..
One is called vectored interrupt and the other, nonvectored interrupt. In a non vectored interrupt, the branch address is assigned to a fixed location in memory.
In a vectored interrupt, the source that interrupts supplies the branch information to the computer. This information is called the interrupt vector.

## Slide 12: Priority Interrupts
Priority
Determines which interrupt is to be served first when two or more requests are made simultaneously
Also determines which interrupts are permitted to interrupt the computer while another is being serviced
Higher priority interrupts can make requests while servicing a lower priority interrupt
A priority interrupt is a system that establishes priority over the various sources to determine
- which condition is to serviced first when two or more requests arrive simultaneously
-which conditions are permitted to interrupt the computer while another request is being serviced

## Slide 13: Priority Interrupts
Priority Interrupt by Software (Polling)
Polling procedure is used to identify highest priority source by software means
common branch address for all the interrupts
  Priority is established by the order of polling the devices(interrupt sources)
- highest priority device is tested first and if interrupt is on , control branches to service routine for this source otherwise next lower priority source is tested
  Flexible since it is established by software
  Low cost since it needs a very little hardware
  Very slow
  if there are many interrupt time required to poll may exceed time available to service IO device

## Slide 14: Priority Interrupts
Priority Interrupt by Hardware
Require a priority interrupt manager which accepts all the interrupt requests to determine the highest priority request.
Fast since identification of the highest priority interrupt request is identified by the hardware
Fast since each interrupt source has its own interrupt vector to access directly to its own service routine
- Can be addressed using serial or parallel connection of interrupt lines.
Example of serial is Daisy chaining Priority

## Slide 15: Hardware Priority Interrupts – Daisy Chain
Interrupt acknowledge
next vice
INT
CPU
INTACK
 | VAD 1 |  |  | VAD 2 |  |  | VAD 3 | 
Device 1 PI PO |  |  | Device 2 PI PO |  |  | Device 3 PI PO |  | To de
 | Interrupt |  |  | request |  |  |  | 
Serial hardware priority function
Interrupt Request Line
  Single common line
Interrupt Acknowledge Line
  Daisy-Chain
-Serial connection of all device that request an interrupt
-Device with highest priority placed in first position followed by devices with lower priority and so on.
-Interrupt generated by any device signals low state interrupt line
-CPU responds by enabling interrupt acknowledgement (INTACK) line.
- device receives PI=1 and passes to next only when not requesting else PI=0
-Thus device with PI=1 and PO=0 is one with highest priority requesting interrupt

## Slide 16
Hardware Priority Interrupts – Daisy Chain
Example: Daisy chain working

## Slide 17: Parallel Priority Interrupts
IEN:
Set or Clear by instructions ION or IOF
IST: Represents an unmasked interrupt has occurred.
INTACK enables tristate Bus Buffer to load VAD generated by the Priority Logic
Interrupt Register:
Each bit is associated with an Interrupt Request from different Interrupt Source - different priority level
Each bit can be cleared by a program instruction
Mask Register:
Mask Register is associated with Interrupt Register
Each bit can be set or cleared by an Instruction

## Slide 18: Parallel Priority Interrupts
Mask register
INTACK
from CPU
I 0
I 1
Priority
I 2 encoder
I 3
0
1
2
3
IST
IEN
0
1
2
3
y |  | 
x |  | 
0 |  | 
0 |  | 
0 |  | 
0 |  | 
0 |  | 
0 |  | 
Disk
Printer
Reader
Keyboard
Interrupt register
Enable
Interrupt to CPU
VAD
to CPU
Bus Buffer

## Slide 19: Priority Encoder
Determines the highest priority interrupt when more than one interrupts take place
Priority Encoder Truth table
Inputs
Outputs
I0 | I1 | I2 | I3 |  | x | y | IST | Boolean functions
1 | d | d | d |  | 0 | 0 | 1 | 
0 | 1 | d | d |  | 0 | 1 | 1 | 
0 | 0 | 1 | d |  | 1 | 0 | 1 | x = I0' I1'
0 | 0 | 0 | 1 |  | 1 | 1 | 1 | y = I0' I1 + I0’ I2’
0 | 0 | 0 | 0 |  | d | d | 0 | (IST) = I0 + I1 + I2 + I3

## Slide 20: Interrupt Cycle
At the end of each Instruction cycle
CPU checks IEN and IST
If IEN · IST = 1, CPU -> Interrupt Cycle
SP ← SP - 1 M[SP] ← PC INTACK ← 1. PC ← VAD IEN ← 0
Decrement stack pointer Push PC into stack
Enable interrupt acknowledge Transfer vector address to PC Disable further interrupts
Go To Fetch to execute the first instruction in the interrupt service routine

## Slide 21: Initial and Final Operations
JMP PTR
JMP RDR
JMP KBD
JMP DISK
0
1
2
3
Program to service
line printer
Program to service character reader
Program to service
keyboard
DISK
PTR
RDR
KBD
255
256
256
750
Stack
Main program
current instr.
749
750
KBD
interrupt
2
VAD=00000011
3
4
Disk
interrupt
5
6
7
Program to service
magnetic disk
8
9
10
11
1

## Slide 22: Initial and Final Operations
Each interrupt service routine must have an initial and final set of operations for controlling the registers in the hardware interrupt system
Initial Sequence
Clear lower level Mask reg. bits
IST <- 0
Save contents of CPU registers
IEN <- 1
Go to Interrupt Service Routine
Final Sequence
IEN <- 0
Restore CPU registers
Clear the bit in the Interrupt Reg
Set lower level Mask reg. bits
Restore return address, IEN <- 1

## Slide 23: Direct Memory Access
Block of data transfer between high speed devices like Disk and Memory
DMA controller - Interface which takes over the buses to manage the transfer directly between
Memory and I/O Device, freeing CPU for other tasks
CPU initializes DMA Controller by sending memory address and the block size (number of words)
Address register:
Contains an address to specify Desired location in memory
Word count register
Holds no. of words to be transferred
Control register
Specifies the mode of transfer

## Slide 24: Direct Memory Access
24
Data bus Read Write
ABUS DBUS
RD WR
Bus request
Bus granted
BR
BG
CPU
Data bus
DMA select
Read Write
Bus request
Bus grant Interrupt
DS
RS RD
WR BR
BG Interrupt
Data bus
buffers
Address bus
buffers
Address register
Word count register
Control register
DMA request
DMA acknowledge
to I/O device
Control logic
Internal Bus
Fig 2: Block diagram of DMA controller
Fig 1: CPU bus signals for DMA transfer
Address bus

## Slide 25: Direct Memory Access
25
RD and WR is bidirectional
When BG=0 CPU can communicate with DMA Register
When BG=1 CPU left the buses and DMA can communicate directly with memory
DMA Transfer can be made in several ways
Burst Transfer : a block sequence consisting of memory words is transferred
in continuous burst while the DMA controller is master of memory bus
- This mode of transfer is needed for fast devices such as magnetic disk where data transmission cannot be stopped or slowed down until an entire block is transferred
Cycle stealing : Alternative technique called cycle stealing allows DMA controller to transfer one data word at time after which it must return control of the buses to the CPU.
- CPU merely delays its operation for one memory cycle to allow the direct memory I/O transfer to “steal” one memory cycle

## Slide 26: DMA I/O Operation
26
DMA is first initialized by CPU. After that DMA starts and continues to transfer data between memory and peripheral unit until an entire block is transferred.
CPU initializes the DMA by sending following information through data bus:
Starting address of the memory block (for read/write)
Word Count (no. of words in memory block)
Control to specify mode of transfer (E.g. read/write)
A control to start DMA Transfer

## Slide 27: DMA Transfer
27
BG
BR
CPU
RD
WR
Addr
Data
Interrupt
Random-access memory unit (RAM)
RD
WR
Addr
Data
BR
BG
WR
Addr
Data
Interrupt
RD DS
RS
DMA
Controller
I/O Peripheral
device
DMA request
DMA ack.
Read control
Write control Data bus Address bus
Address select

## Slide 28: I/O Processor - Channel
28
Channel
Processor with direct memory access capability that communicates with I/O devices
Channel accesses memory by cycle stealing
Unlike DMA Controller, IOP can fetch and execute its own instruction
IOP Instructions (Commands) specially designed to facilitate I/O transfer.
  Data gathered in IOP at device rate and bit capacity while CPU executing own program
  Transfer between IOP and Device similar to Programmed I/O and transfer between IOP and Memory similar to DMA
  CPU is master while IOP is slave processor
- CPU initiates the channel by executing a channel I/O class instruction and once initiated, channel operates independent of the CPU
PD
PD
Peripheral devices
PD PD
I/O bus
Input-output processor (IOP)
Central processing unit (CPU)
Memory unit
Memory Bus

## Slide 29: Channel CPU Communication
29
Send instruction to test IOP.path
If status OK, then send start I/O instruction
to IOP.
CPU continues with another program
Transfer status word
to memory
Access memory for IOP program
Conduct I/O transfers using DMA;
Prepare status report.
I/O transfer completed; Interrupt CPU
Request IOP status
Transfer status word to memory location
Check status word for correct transfer.
Continue
CPU operations
IOP operations