## Slide 1: DATA AND SIGNALS

## Slide 2: To be transmitted, data must be transformed to electromagnetic signals.

## Slide 3: ANALOG AND DIGITAL
Data can be analog or digital. The term analog data refers to information that is continuous; digital data refers to information that has discrete states. Analog data take on continuous values. Digital data take on discrete values.
Topics discussed in this section:
Analog and Digital Data Analog and Digital Signals
Periodic and Nonperiodic Signals

## Slide 4: Data can be analog or digital. Analog data are continuous and take continuous values.
Note
Digital data have discrete states and take discrete values.

## Slide 5: Signals can be analog or digital. Analog signals can have an infinite number of values in a range; digital signals can have only a limited number of values.
Note

## Slide 6: Comparison of analog and digital signals

## Slide 7: Periodic and Non Periodic
A periodic signal completes a pattern within a measurable time frame, called a period, and repeats that pattern over subsequent identical periods.
The completion of one full pattern is called as a cycle.
A non-periodic signal changes without exhibiting a pattern or a cycle.

## Slide 8: Note
In data communications, we commonly use periodic analog signals and nonperiodic digital signals.

## Slide 9
PErIoDIc ANAloG SIGNAlS
Periodic analog signals can be classified as simple or composite.

## Slide 10: Figure A sine wave

## Slide 11
A sine wave is represented by:
Peak Amplitude
Frequency
Phase
Wavelength

## Slide 12: Peak Amplitude
The peak
amplitude of a signal
is the
absolute value of its highest
intensity,
proportional to energy it carries.
Measured in volts.

## Slide 13
Two signals with the same phase and frequency,
but different amplitudes

## Slide 14: Example
The voltage of a battery is a constant; this constant value can be considered a sine wave, as we will see later. For example, the peak value of an AA battery is normally
1.5 V.

## Slide 15: Period and Frequency
Period refers to amount of time, in seconds, a signal takes to complete one cycle.
Frequency refers to the number of periods in 1 second.
Period is expressed in seconds and frequency is expressed in hertz (Hz)

## Slide 16: Note
Frequency and period are the inverse of each other.

## Slide 17: Note
Frequency is the rate of change with respect to time.
Change in a short span of time means high frequency.
Change over a long span of time means low frequency.

## Slide 18: Note
If a signal does not change at all, its frequency is zero.
If a signal changes instantaneously, its frequency is infinite.

## Slide 19: Table Units of period and frequency

## Slide 20: Figure
Two signals with the same amplitude and phase,
but different frequencies

## Slide 21
The power we use at home has a frequency of 60 Hz. Determined the period of this sine wave?
Example

## Slide 22
Express a period of 100 ms in microseconds.
Example

## Slide 23: Example
The period of a signal is 100 ms. What is its frequency in kilohertz?
Solution

## Slide 24: Note
Phase describes the position of the waveform relative to time 0.

## Slide 25: Figure
Three sine waves with the same amplitude and frequency,
but different phases

## Slide 26
A sine wave with value 1/6 cycle with respect to time 0. What is its phase in degrees and radians?
Example

## Slide 27: Figure
Wavelength and period

## Slide 28: Wavelength
Wavelength is the distance a signal can travel in one period.
Wavelength= propagation speed* period
Or
Wavelength= propagation speed/ frequency

## Slide 29: Figure
The time-domain and frequency-domain plots of a sine wave

## Slide 30: Note
A complete sine wave in the time domain can be represented by one single spike in the frequency domain.

## Slide 31: Example
The frequency domain is more compact and useful when we are dealing with more than one sine wave. For example, Figure 3.8 shows three sine waves, each with different amplitude and frequency. All can be represented by three spikes in the frequency domain.

## Slide 32: Figure
The time domain and frequency domain of three sine waves

## Slide 33
A single-frequency sine wave is not useful in data communications;
we need to send a composite signal, a signal made of many simple sine waves.
Note

## Slide 34: Note
According to Fourier analysis, any composite signal is a combination of simple sine waves with different frequencies, amplitudes, and phases.

## Slide 35: If the composite signal is periodic, the decomposition gives a series of signals with discrete frequencies; if the composite signal is nonperiodic, the decomposition gives a combination of sine waves with continuous frequencies.
Note

## Slide 36: Example
Figure 3.9 shows a periodic composite signal with frequency f. This type of signal is not typical of those found in data communications. We can consider it to be three alarm systems, each with a different frequency. The analysis of this signal can give us a good understanding of how to decompose signals.

## Slide 37: Figure A composite periodic signal

## Slide 38: Figure
Decomposition of a composite periodic signal in the time and
frequency domains

## Slide 39: Example
Figure 3.11 shows a nonperiodic composite signal. It can be the signal created by a microphone or a telephone set when a word or two is pronounced. In this case, the composite signal cannot be periodic, because that implies that we are repeating the same word or words with exactly the same tone.

## Slide 40: Figure The time and frequency domains of a nonperiodic signal

## Slide 41
The bandwidth of a composite signal is the difference between the
highest and the lowest frequencies contained in that signal.
Note

## Slide 42: Figure
The bandwidth of periodic and nonperiodic composite signals

## Slide 43: Example
If a periodic signal is decomposed into five sine waves with frequencies of 100, 300, 500, 700, and 900 Hz, what is its bandwidth? Draw the spectrum, assuming all components have a maximum amplitude of 10 V. Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
The spectrum has only five spikes, at 100, 300, 500, 700,
and 900 Hz (see Figure 3.13).

## Slide 44: Figure The bandwidth for Example 3.10

## Slide 45: Example
A periodic signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz. What is the lowest frequency? Draw the spectrum if the signal contains all frequencies of the same amplitude.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
The spectrum contains all integer frequencies. We show this by a series of spikes (see Figure 3.14).

## Slide 46: Figure The bandwidth for Example 3.11

## Slide 47: Example
A nonperiodic composite signal has a bandwidth of 200 kHz, with a middle frequency of 140 kHz and peak amplitude of 20 V. The two extreme frequencies have an amplitude of 0. Draw the frequency domain of the signal.
Solution
The lowest frequency must be at 40 kHz and the highest at 240 kHz. Figure 3.15 shows the frequency domain and the bandwidth.

## Slide 48: Figure
The bandwidth for Example 3.12

## Slide 49: 3-3 DIGItAl SIGNAlS
In addition to being represented by an analog signal, information can also be represented by a digital signal. For example, a 1 can be encoded as a positive voltage and a 0 as zero voltage. A digital signal can have more than two levels. In this case, we can send more than 1 bit for each level.

## Slide 50: Figure
Two digital signals: one with two signal levels and the other
with four signal levels

## Slide 51: Example
A digital signal has eight levels. How many bits are needed per level? We calculate the number of bits from the formula
Each signal level is represented by 3 bits.

## Slide 52: Example
A digital signal has nine levels. How many bits are needed per level? We calculate the number of bits by using the formula. Each signal level is represented by
3.17 bits. However, this answer is not realistic. The number of bits sent per level needs to be an integer as well as a power of 2. For this example, 4 bits can represent one level.

## Slide 53: Bit Rate
Most Digital Signals are non-periodic. Therefore, period and frequency are not appropriate characteristics.
Bit rate is used.
Bit rate is number of bits sent in 1s. Expressed in
bps.

## Slide 54: Example
Assume we need to download text documents at the rate of 100 pages per minute. What is the required bit rate of the channel?
Solution
A page is an average of 24 lines with 80 characters in each line. If we assume that one character requires 8 bits, the bit rate is

## Slide 55: Bit Length
Bit length is distance one bit occupies on transmission medium.
Bit length= propagation speed* bit duration

## Slide 56: Figure
Baseband transmission

## Slide 57: Note
A digital signal is a composite analog signal with an infinite bandwidth.

## Slide 58: Figure
Bandwidths of two low-pass channels

## Slide 59: Figure Baseband transmission using a dedicated medium

## Slide 60: Note
Baseband transmission of a digital signal that preserves the shape of the digital signal is possible only if we have a low-pass channel with an infinite or very wide bandwidth.

## Slide 61: Note
In baseband transmission, the required bandwidth is
proportional to the bit rate;
if we need to send bits faster, we need more bandwidth.
In baseband transmission, the required bandwidth is proportional to the bit rate; if we need to send bits faster, we need more bandwidth. Bit rate is twice the bandwidth required.

## Slide 62: Broadband Transmission: Bandwidth of a bandpass channel

## Slide 63: Note
If the available channel is a bandpass channel, we cannot send the digital signal directly to the channel;
we need to convert the digital signal to an analog signal before transmission.

## Slide 64: Figure
Modulation of a digital signal for transmission on a bandpass
channel

## Slide 65: Example
An example of broadband transmission using modulation is the sending of computer data through a telephone subscriber line, the line connecting a resident to the central telephone office. These lines are designed to carry voice with a limited bandwidth. The channel is considered a bandpass channel. We convert the digital signal from the computer to an analog signal, and send the analog signal. We can install two converters to change the digital signal to analog and vice versa at the receiving end. The converter, in this case, is called a modem

## Slide 66: DAtA rAtE lIMItS
A very important consideration in data communications is how fast we can send data, in bits per second, over a channel. Data rate depends on three factors:
The bandwidth available
The level of the signals we use
The quality of the channel (the level of noise)
Topics discussed in this section: Noiseless Channel: Nyquist Bit Rate Noisy Channel: Shannon Capacity Using Both Limits

## Slide 67: Note
Increasing the levels of a signal may reduce the reliability of the system.

## Slide 68
Noiseless Channel: Nyquist Bit Rate
Bit Rate= 2 * bandwidth * log2 L

## Slide 69
Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels. The maximum bit rate can be calculated as
Example

## Slide 70
Consider the same noiseless channel transmitting a signal with four signal levels (for each level, we send 2 bits). The maximum bit rate can be calculated as
Example

## Slide 71: Example
We need to send 265 kbps over a noiseless channel with a bandwidth of 20 kHz. How many signal levels do we need?
Solution
We can use the Nyquist formula as shown:
Since this result is not a power of 2, we need to either increase the number of levels or reduce the bit rate. If we have 128 levels, the bit rate is 280 kbps. If we have 64 levels, the bit rate is 240 kbps.

## Slide 72: Noisy Channel : Shannon Capacity
Capacity= Bandwidth * log2( 1+SNR)

## Slide 73: Example
Consider an extremely noisy channel in which the value of the signal-to-noise ratio is almost zero. In other words, the noise is so strong that the signal is faint. For this channel the capacity C is calculated as
This means that the capacity of this channel is zero regardless of the bandwidth. In other words, we cannot receive any data through this channel.

## Slide 74: Example
We can calculate the theoretical highest bit rate of a regular telephone line. A telephone line normally has a bandwidth of 3000. The signal-to-noise ratio is usually 3162. For this channel the capacity is calculated as
This means that the highest bit rate for a telephone line is 34.860 kbps. If we want to send data faster than this, we can either increase the bandwidth of the line or improve the signal-to-noise ratio.

## Slide 75: Example
The signal-to-noise ratio is often given in decibels. Assume that SNRdB = 36 and the channel bandwidth is 2 MHz. The theoretical channel capacity can be calculated as

## Slide 76: Example
For practical purposes, when the SNR is very high, we can assume that SNR + 1 is almost the same as SNR. In these cases, the theoretical channel capacity can be simplified to
For example, we can calculate the theoretical capacity of the previous example as

## Slide 77: Example
We have a channel with a 1-MHz bandwidth. The SNR for this channel is 63. What are the appropriate bit rate and signal level?
Solution
First, we use the Shannon formula to find the upper limit.

## Slide 78: Example
The Shannon formula gives us 6 Mbps, the upper limit. For better performance we choose something lower, 4 Mbps, for example. Then we use the Nyquist formula to find the number of signal levels.

## Slide 79: Note
The Shannon capacity gives us the upper limit; the Nyquist formula tells us how many signal levels we need.

## Slide 80: 3-6 PErForMANcE
One important issue in networking is the performance of the network—how good is it?.
Topics discussed in this section:
Bandwidth Throughput Latency (Delay)
Bandwidth-Delay Product

## Slide 81: Note
In networking, we use the term bandwidth in two contexts.
❏ The | first, bandwidth in hertz, | refers | to
the | range of frequencies | in | a
range of
composite frequencies
signal that a
or the channel can
pass.
❏ The
second, refers to the speed of
second, bandwidth in bits per
bit
transmission in a channel or link.

## Slide 82
If the telephone company improves the quality of the line and increases the bandwidth to 8 kHz, we can send 112,000 bps by using the same technology
Example

## Slide 83: Example
A network with bandwidth of 10 Mbps can pass only an average of 12,000 frames per minute with each frame carrying an average of 10,000 bits. What is the throughput of this network?
Solution
We can calculate the throughput as
The throughput is almost one-fifth of the bandwidth in this case.

## Slide 84: Latency (Delay)
Latency= Propagation Time+ transmission time +
queuing time+ processing delay

## Slide 85: Example
What is the propagation time if the distance between the two points is 12,000 km? Assume the propagation speed to be 2.4 × 108 m/s in cable.
Solution
We can calculate the propagation time as
The example shows that a bit can go over the Atlantic Ocean in only 50 ms if there is a direct cable between the source and the destination.

## Slide 86: Example
What are the propagation time and the transmission time for a 2.5-kbyte message (an e-mail) if the bandwidth of the network is 1 Gbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Solution
We can calculate the propagation and transmission time as shown on the next slide:

## Slide 87: Example
Note that in this case, because the message is short and the bandwidth is high, the dominant factor is the propagation time, not the transmission time. The transmission time can be ignored.

## Slide 88: Example
What are the propagation time and the transmission time for a 5-Mbyte message (an image) if the bandwidth of the network is 1 Mbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Solution
We can calculate the propagation and transmission times as shown on the next slide.

## Slide 89: Example
Note that in this case, because the message is very long and the bandwidth is not very high, the dominant factor is the transmission time, not the propagation time. The propagation time can be ignored.