## Slide 1: CSE211
1
Computer Organization and Design
Lecture : 3
Tutorial: 1
Practical: 0
Credit: 4

## Slide 2: Overview
2
CSE 211
Register Transfer Language
Register Transfer
Bus and Memory Transfers
Logic Micro-operations
Shift Micro-operations
Arithmetic Logic Shift Unit

## Slide 3
How much storage capacity does each stage in a shift register represent?
One bit
Two bits
Four bits
Eight bits

## Slide 4
The bus used to connect the monitor to the CPU is
PCI bus
SCSI bus
Memory bus
Rambus

## Slide 5: Tri-state Buffer Switch Equivalent
When activated into its third state it disables or turns “OFF” its output producing an open circuit condition that is neither at a logic “HIGH” or “LOW”, but instead gives an output state of very high impedance, High-Z, or more commonly Hi-Z. Then this type of device has two logic state inputs, “0” or a “1” but can produce three different output states, “0”, “1” or ” Hi-Z ” which is why it is called a “Tri” or “3-state” device.
Note that this third state is NOT equal to a logic level “0” or “1”, but is an high impedance state in which the buffers output is electrically disconnected from the rest of the circuit. As a result, no current is drawn from the supply.

## Slide 7: Connecting Registers - Bus Transfer
7

## Slide 8: Connecting Registers - Bus Transfer
8

## Slide 9: Memory Transfer
9
AR
Memory unit
Read
Write
Data out Data in
Memory is usually accessed in computer systems by putting the desired address in a special register, the Memory Address Register (MAR, or AR)
M

## Slide 10: Memory Read
10
To read a value from a location in memory and load it into a register, the register transfer language notation looks like this:
R1  M[MAR]
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Read (= 1) gets sent to the memory unit
  The contents of the specified address are put on the memory’s output data lines
  These get sent over the bus to be loaded into register R1

## Slide 11: Memory Write
11
To write a value from a register to a location in memory looks like this in register transfer language:
M[MAR]  R1
This causes the following to occur
  The contents of the MAR get sent to the memory address lines
  A Write (= 1) gets sent to the memory unit
  The values in register R1 get sent over the bus to the data input lines of the memory
  The values get loaded into the specified address in the memory

## Slide 12
12
,
SUMMARY OF R. TRANSFER MICROOPERATIONS
A  B 1.Transfer content of reg. B into reg. A A  constant 3.Transfer a binary constant into reg. A ABUS  R1, R2 ← ABUS 4.Transfer content of R1 into bus A and, at the same time transfer content of bus A into R2 AR 5.Address register DR 6.Data register M[R] 7.Memory word specified by reg. R M 8.Equivalent to M[AR] DR  M 9.Memory read operation: transfers content of memory word specified by AR into DR M  DR 10.Memory write operation: transfers content of DR into memory word specified by AR

## Slide 13: MICROOPERATIONS
13
Computer system microoperations are of four types:
Register transfer microoperations
Arithmetic microoperations
Logic microoperations
Shift microoperations

## Slide 14: Arithmetic MICROOPERATIONS
14
R3  R1 + R2 R3  R1 - R2 R2  R2’
R2  R2’+ 1
R3  R1 + R2’+ 1 R1  R1 + 1
R1  R1 - 1
Contents of R1 plus R2 transferred to R3 Contents of R1 minus R2 transferred to R3 Complement the contents of R2
2's complement the contents of R2 (negate) subtraction
Increment Decrement
•
The basic arithmetic microoperations are
–
–
–
–
Addition Subtraction Increment Decrement
•
The additional arithmetic microoperations are
–
–
–
–
Add with carry Subtract with borrow Transfer/Load
etc. …
Summary of Typical Arithmetic Micro-Operations

## Slide 15: Full Adder
is the adder which
adds three inputs and produces two outputs. The first two inputs are A and B and the third input is an input carry as C-IN. The output carry is designated as C-OUT and the normal output is designated as S which is SUM.

## Slide 16: Binary Adder
16

## Slide 17: Binary Adder-Subtractor
17
Binary Adder-Subtractor
FA
B0 A0
S0
C0
C1
FA
B1 A1
S1
C2
FA
B2 A2
C3
FA
B3 A3
S3 S2
C4
M
Mode input M controls the operation
  M=0 ---- adder
  M=1 ---- subtractor

## Slide 18: Binary Incrementer
18
Binary Incrementer
x y
HA
C
S
A0
1
S0
x y
HA
C
S
A1
S1
x
HA
y
C
S
A2
S2
x
HA
y
C
S
A3
C4 S3

## Slide 19: Arithmetic Circuits
19
S1 S0
0
1
4x1
2 MUX
3
D0
X0 C0
FA
Y0 C1
S1 S0
0
1
4x1
2 MUX
3
D1
X1 C1
FA
Y1 C2
S1 S0
0
1
4x1
2 MUX
3
D2
X2 C2
FA
Y2 C3
S1 S0
0
1
4x1
2 MUX
3
D3
X3 C3
FA
Y3 C4
Cout
A0
B0
A1
B1
A2
B2
A3
B3
0 1
Cin
S1 S0