## Slide 1: CSE211
1
Computer Organization and Design
Lecture : 3
Tutorial: 1
Practical: 0
Credit: 4

## Slide 2: MICROOPERATIONS
2
CSE 211
Computer system microoperations are of four types:
Arithmetic microoperations
Register transfer microoperations
Logic microoperations
Shift microoperations

## Slide 3: Arithmetic MICROOPERATIONS
3
CSE 211
R3  R1 + R2 R3  R1 - R2 R2  R2’
R2  R2’+ 1
R3  R1 + R2’+ 1 R1  R1 + 1
R1  R1 - 1
Contents of R1 plus R2 transferred to R3 Contents of R1 minus R2 transferred to R3 Complement the contents of R2
2's complement the contents of R2 (negate) subtraction
Increment Decrement
•
The basic arithmetic microoperations are
–
–
–
–
Addition Subtraction Increment Decrement
•
The additional arithmetic microoperations are
–
–
–
–
Add with carry Subtract with borrow Transfer/Load
etc. …
Summary of Typical Arithmetic Micro-Operations

## Slide 4: Full Adder
is the adder which
adds three inputs and produces two outputs. The first two inputs are A and B and the third input is an input carry as C-IN. The output carry is designated as C-OUT and the normal output is designated as S which is SUM.

## Slide 5: Binary Adder
5
CSE 211

## Slide 6
◦
The augend bits (A) and the addend bits (B) are designated by subscript numbers from right to left, with subscript '0' denoting the low-order bit.
The carry inputs starts from C0 to C3 connected in a chain through the full-adders. C4 is the resultant output carry generated by the last full-adder circuit.
The output carry from each full-adder is connected to the input carry of the next-high-order full-adder.
The sum outputs (S0 to S3) generates the required arithmetic sum of augend and addend bits.
The n data bits for the A and B inputs come from different source registers. For instance, data bits for A input comes from source register R1 and data bits for B input comes from source register R2. The arithmetic sum of the data inputs of A and B can be transferred to a third register or to one of the source registers (R1 or R2).
◦
◦
◦
◦
◦

## Slide 7: BINARY ADDER-SUBTRACTOR
Mode input M controls the operation
  M=0 ---- adder
  M=1 ---- subtractor

## Slide 8
◦
When the mode input (M) is at a low logic, i.e. '0', the circuit act as an adder and when the mode input is at a high logic, i.e. '1', the circuit act as a subtractor.
The exclusive-OR gate connected in series receives input M and one of the inputs B.
When M is at a low logic, we have BⒸ 0 = B.
The full-adders receive the value of B, the input carry is 0, and the circuit performs A plus B.
When M is at a high logic, we have BⒸ 1 = B' and C0 = 1.
The B inputs are complemented, and a 1 is added through the input carry. The circuit performs the operation A plus the 2's complement of B.
◦
◦
◦
◦

## Slide 9: BINARY INCREMENTER
The increment micro-operation adds one binary value to the value of binary variables stored in a register. For instance, a 4-bit register has a binary value 0110, when incremented by one the value becomes 0111. The increment micro-operation is best implemented by a 4-bit combinational circuit incrementer. A 4-bit combinational circuit incrementer can be represented by the following block diagram.

## Slide 10
A logic-1 is applied to one of the inputs of least significant half-adder, and the other input is connected to the least significant bit of the number to be incremented.
The output carry from one half-adder is connected to one of the inputs of the next-higher-order half-adder.
The binary incrementer circuit receives the four bits from A0 through A3, adds one to it, and generates the incremented output in S0 through S3.
The output carry C4 will be 1 only after incrementing binary 1111.

## Slide 13: Arithmetic Circuits
13
CSE 211
S1 S0
0
1
4x1
2 MUX
3
D0
X0 C0
FA
Y0 C1
S1 S0
0
1
4x1
2 MUX
3
D1
X1 C1
FA
Y1 C2
S1 S0
0
1
4x1
2 MUX
3
D2
X2 C2
FA
Y2 C3
S1 S0
0
1
4x1
2 MUX
3
D3
X3 C3
FA
Y3 C4
Cout
A0
B0
A1
B1
A2
B2
A3
B3
0 1
Cin
S1 S0