## Slide 1: DATA LINK CONTROL

## Slide 2: Data Link Layer Design Issues
Services Provided to the Network Layer
Framing
Error Control
Flow Control

## Slide 3: FRAMING
The data link layer needs to pack bits into frames, so that each frame is distinguishable from another. Our postal system practices a type of framing. The simple act of inserting a letter into an envelope separates one piece of information from another; the envelope serves as the delimiter.
Topics discussed in this section:
Fixed-Size Framing Variable-Size Framing

## Slide 4: Types of Framing
Fixed Size Framing
Variable | Size Framing--- | Character
oriented | protocols and Bit | oriented
Protocols. |  | 

## Slide 5: A frame in a character-oriented protocol

## Slide 6: Byte stuffing and unstuffing

## Slide 7: Note
Byte stuffing is the process of adding 1 extra byte whenever there is a flag or escape character in the text.

## Slide 8: A frame in a bit-oriented protocol

## Slide 9: Bit stuffing is the process of adding one extra 0 whenever five consecutive 1s follow a 0 in the data, so that the receiver does not mistake the pattern 0111110 for a flag.
Note

## Slide 10: Bit stuffing and unstuffing

## Slide 11: FLOW AND ERROR CONTROL
The most important responsibilities of the data link layer are flow control and error control. Collectively, these functions are known as data link control.
Topics discussed in this section:
Flow Control
Error Control

## Slide 12
Flow control refers to a set of procedures used to restrict the amount of data
that the sender can send before waiting for acknowledgment.
Note

## Slide 13: Note
Error control in the data link layer is based on automatic repeat request, which is the retransmission of data.

## Slide 14: Taxonomy of protocols discussed in this chapter

## Slide 15: NOISELESS CHANNELS
Let us first assume we have an ideal channel in which no frames are lost, duplicated, or corrupted. We introduce two protocols for this type of channel.
Topics discussed in this section:
Simplest Protocol
Stop-and-Wait Protocol

## Slide 16: Simplest Protocol
No flow and Error Control

## Slide 17: The design of the simplest protocol with no flow or error control

## Slide 18: Flow diagram for Simplest

## Slide 19: Stop-and-Wait Protocol
Sender sends one frame, stops until it gets confirmation from receiver.

## Slide 20: Design of Stop-and-Wait Protocol

## Slide 21: Flow diagram for Stop and Wait

## Slide 22: NOISY CHANNELS
Although the Stop-and-Wait Protocol gives us an idea of how to add flow control to its predecessor, noiseless channels are nonexistent. We discuss three protocols in this section that use error control.
Topics discussed in this section:
Stop-and-Wait Automatic Repeat Request Go-Back-N Automatic Repeat Request Selective Repeat Automatic Repeat Request

## Slide 23: Note
In Stop-and-Wait ARQ, we use sequence numbers to number the frames.
The sequence numbers can be 1,0,1,0,1…

## Slide 24: Note
In Stop-and-Wait ARQ, the acknowledgment number is 0 if sequence number is 1 and acknowledgment number is 1 if sequence number is 0

## Slide 25: Design of the Stop-and-Wait ARQ Protocol

## Slide 26: Flow diagram for Example 11.3

## Slide 27: Disadvantage Stop-and-Wait ARQ Protocol
Inefficient---if channel is thick and long
Thick means high bandwidth
Long means roundtrip delay
Product of both is bandwidth delay.
Bandwidth delay is number of bits we can send while waiting for news from receiver.

## Slide 28: Assume that, in a Stop-and-Wait ARQ system, the bandwidth of the line is 1 Mbps, and 1 bit takes 20 ms to make a round trip. What is the bandwidth-delay product? If the system data frames are 1000 bits in length, what is the utilization percentage of the link?
11.28
Solution
The bandwidth-delay product is

## Slide 29: Pipelining
Task begins before end of first task.
Stop-and-Wait ARQ does not use pipelining but other two techniques do.
This improves efficiency.

## Slide 30: Go-Back-N Protocol
This sends multiple frames before receiving acknowledgment from receiver.

## Slide 31
In the Go-Back-N Protocol, the sequence numbers are modulo 2m,
where m is the size of the sequence number field in bits.
Note

## Slide 32: Sliding Window
Defines the range of sequence numbers that is concern of sender and receiver.
The range which is concern of sender is called sender sliding window.
The range which is concern of receiver is called receiver sliding window.

## Slide 33: Send window for Go-Back-N ARQ

## Slide 34: Note
The send window is an abstract concept defining an imaginary box of size 2m − 1 with three variables: Sf, Sn, and Ssize.

## Slide 35: Note
The send window can slide one or more slots when a valid acknowledgment arrives.

## Slide 36: Receive window for Go-Back-N ARQ

## Slide 37: The receive window is an abstract concept defining an imaginary box of size 1 with one single variable Rn. The window slides
when a correct frame has arrived; sliding occurs one slot at a time.
Note

## Slide 38: Design of Go-Back-N ARQ

## Slide 39: Note
In Go-Back-N ARQ, the size of the send window must be less than 2m;
the size of the receiver window is always 1.

## Slide 40: Flow diagram

## Slide 41: Flow diagram

## Slide 42: Note
Stop-and-Wait ARQ is a special case of Go-Back-N ARQ in which the size of the send window is 1.

## Slide 43: Send window for Selective Repeat ARQ

## Slide 44: Receive window for Selective Repeat ARQ

## Slide 45: Design of Selective Repeat ARQ

## Slide 46
In Selective Repeat ARQ, the size of the sender and receiver window
must be at most one-half of 2m.
Note

## Slide 47: Delivery of data in Selective Repeat ARQ

## Slide 48: Flow diagram

## Slide 49: Design of piggybacking in Go-Back-N ARQ